## Slide 1: New Hardware Enabling New User Experiences
James Scott
Sensors and Devices Group
Microsoft Research Cambridge

## Slide 2: Sensors and Devices group
Alex Butler
Steve Hodges
James Scott
Shahram Izadi
Nicolas Villar
Emma Berry
Darren West
David Molyneaux
Mike
Hazas

## Slide 3: Sensors and Devices group
hardware
software
user experience
Compelling new user experiences are driven by innovation throughout the stack

## Slide 4: Sensors and Devices group
PCB layout
industrial design
optics
materials
mechanics
manufacturing
user interface
networking
computer vision
graphics
drivers
rendering
wireless
low-power
P2P
application development
circuit design
devices
Interaction techniques
sensing
signal processing
displays
sensor fusion
haptics
hardware
software
user experience
graphic design

## Slide 5: Four Projects
SenseCam
Somniloquy
Force Sensing
SecondLight
  Live Demo

## Slide 6: SenseCam
Emma Berry, Steve Hodges, Georgina Browne, et al.

## Slide 7: SenseCam
A new concept for digital cameras
  wearable, wide-angle lens
  automatic capture
  range of sensors
New media type
  between digital stills & video
  ‘digital experience’ capture
Applications
  sharing experiences with others
  cueing recall for the wearer

## Slide 8: SenseCam Video

## Slide 9: Clinical studies: case study 1
Mrs B
(Berry et al., 2007)
Cambridge Memory Clinic
63 year old, well educated woman
Limbic encephalitis 2002
Severe episodic memory impairment
  No recall of an event within 3 to 5 days

## Slide 10: Results
Memory of an event over time
Time elapsed since event
% Recall
Written diary
SenseCam
Baseline
(days)
Chart: 
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | +1m | +2m | +3m | +10m
 | 8 | 6 | 1 | 1 | 1 | 1 | 1
 | 59 | 43 | 55 | 36 | 43 | 52 | 49 | 1
 | 30 | 42 | 56 | 64 | 68 | 68 | 83 | 80 | 67 | 76 | 80

## Slide 11: Results
Time elapsed since event
% Recall
Written diary
SenseCam
Baseline
(days)
Chart: 
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | +1m | +2m | +3m | +10m
 | 8 | 6 | 1 | 1 | 1 | 1 | 1
 | 59 | 43 | 55 | 36 | 43 | 52 | 49 | 1
 | 30 | 42 | 56 | 64 | 68 | 68 | 83 | 80 | 67 | 76 | 80
Memory of an event over time

## Slide 12: fMRI Study with Mrs B
Studying physiological effects of SenseCam using fMRI machine

## Slide 13: Design
  Experimental condition (‘SenseCam’)
    Trip away 4.5 weeks before scan
    SenseCam used to rehearse memorable weekend
    Rehearsal continued until 1 week before scan
    50 images presented
  Control condition (‘Written’)
    Trip away 3.5 weeks before scan
    Written diary used to rehearse memorable weekend
    Rehearsal continued until day of scan
    50 images presented

## Slide 14: Design
  Control condition (‘Not Reviewed’)
    Trip away 6.5 weeks before scan
    No rehearsal of memorable weekend
    25 images presented
  Control condition (‘Novel’)
    Another person’s images viewed while being scanned
    25 images presented

## Slide 15: User interface inside fMRI

## Slide 16: Behavioural results
Not reviewed v novel: not significant
SC v written:
p<0.001

## Slide 17: fMRI Study: Novel v. Not Reviewed
No significant differences in brain activity

## Slide 18: SenseCam v. Written

## Slide 19: Summary
Mrs B is no more likely to recognise pictures from an experienced, not reviewed event, than novel pictures, with no brain differences
SenseCam helps Mrs B to recall events more effectively than a diary or no method at all
When viewing SenseCam images, activity is observed across a network of regions involved in autobiographical memory

## Slide 20: Somniloquy* Augmenting Network Interfaces to Reduce PC Energy Usage
Yuvraj Agarwal, Steve Hodges, Ranveer Chandra, James Scott, Victor Bahl, Rajesh Gupta
*som-nilo-quy (noun): The act or habit of talking while asleep.

## Slide 21: Motivation
Users leave PCs on instead of putting them in sleep mode, causing:
  Monetary cost
  Environmental cost
  Laptops: shorter battery life
  Heat/noise
We propose a simple hardware modification allowing absent users’ needs from their PCs to be achievable while the PC is asleep

## Slide 22: Why do people leave PCs on?
Motivating survey of 107 computer users
Respondents regularly left 75% of office PCs and 30% of home PCs on unattended
Chart: %ge of respondents stating application as reason PC is left on when no user is present
| File downloading | Email/IM client | Network server of some type | Other application
Home (N=62) | 40.3226 | 37.0968 | 17.7419 | 14.5161
Office (N=47) | 2.1277 | 46.8085 | 25.5319 | 29.7872
What apps do you leave running on your computer?

## Slide 23: Somniloquy overview
Augment NIC with a low-power domain which stays on when the PC is asleep
Same MAC and IP address → transparent to network and to remote servers
Wake the PC up on specified events at any layer e.g. incoming connection
Handles some application functionality while PC remains asleep using “application stubs”
Somniloquy
daemon
Host processor,
RAM, peripherals, etc.
Operating system, including networking stack
Apps
Network interface hardware
Secondary processor
Embedded CPU, RAM, flash
Embedded OS, incl. networking stack
Port filters
Appln stubs
Host PC

## Slide 24: Prototype
Prototype uses “gumstix” platform
  PXA270 processor with full TCP/IP stack
  USB connection to PC for sleep detection/wakeup trigger, power whilst asleep, and IP networking for data
Wired (802.3) and wireless (802.11) versions implemented
Wired prototype
Wireless prototype

## Slide 25: Applications
Home PCs
  Continue to perform file downloads during sleep (gumstix downloads file onto SD card, wakes PC when finished)
  Ready for remote access (e.g. Xbox media center) while asleep
Office PCs
  Ready for remote desktop login even while asleep
  Management functions – e.g. Patches to OS or software
Mobile PCs
  Extend battery life by performing functions while asleep
  Stay logged in to “presence” servers, e.g. For incoming instant messages or voice calls, even while mobile

## Slide 26: Power Savings
Gumstix prototype draws 250mW (idle) to 1.6W (fully active)
For test desktop, power drops from >100W to <5W, i.e. 620kWh saved per year (~£35, ~378 kg CO2)
For test laptop, power drops from >10W to ~1W, battery life increases from <6 hours to >60 hours
Dell Optiplex 745 Power Consumption

## Slide 27: Somniloquy Video

## Slide 28: Offloading File Sharing
To address P2P file sharing, we run a simple bittorrent client on the gumstix
  Downloads (and uploads) files while the PC is asleep using 2Gb SD card
  Wakes the PC up e.g. when download completes, when SD card is full, or when a peer requests a file on the hard disk
  Uses 16% of CPU when downloading, and fits easily into the 64Mb RAM

## Slide 29: Conclusions
Somniloquy is an architecture augmenting NICs to be network-connected while the PC is asleep
Allows the millions of office PCs left on e.g. for RDP/SMB, and home PCs left on e.g. for file sharing, to accomplish these tasks by “talking in their sleep”
Savings of ~100W per desktop

## Slide 30: Mobile Device Interaction with Force Sensing
James Scott, Lorna Brown and Mike Molloy

## Slide 31: Force Sensing
Sense forces that a user applies to the device casing
Makes casing an active input region
Device does NOT need to deform (key difference to related work e.g. Gummi)
Stretching/Compressing
Squeezing, Steering
Twisting, Screwing
Bending, Folding
Four force “gestures”

## Slide 32: Qualities of Force Sensing
Adds sensing capability to unused casing areas of devices
Avoids “clutter” of controls on device
Usable without obscuring the screen
Two-handed or potentially one-handed
May be useful for context sensing outside interaction, e.g. “Am I under something”
Useful in combination with other inputs

## Slide 33
Force sensors
on top of metal
tongues (2 more
underneath)
Screw through
casing and
metal layer
Metal layer
Acrylic
layers
Phidgets analog interface kit
USB data
port
Samsung Q1 UMPC
Prototype based on Augmented UMPC
Sensors could be built inside casing in future

## Slide 34: Force-Based Interaction Example
Provide “shortcut keys” on mobile devices w/out keyboards
  Twist for alt-tab
  Bend for page-down/up
Visual feedback matches force
  Makes it really easy to learn, like many touch-based gestures
  Compare to “alt-tab”
Avoids:
  Putting lots of buttons on bezel
  Using screen real-estate on virtual buttons
Other uses also possible
  E.g. Scrolling/zooming, 3D CAD, ...

## Slide 35: Force Sensing Video

## Slide 36
Force cursor
Inactive targets
Active target
Currently selected target
Participant either twists (9 users) or bends (9 other users)
Twisting/bending moves a “force cursor” left or right
Once an “active target” is highlighted, participant moves force cursor over it and holds it there for 2 seconds to make it inactive
Participant then returns back to zero force before next target
User
Study

## Slide 37
Force cursor
Inactive targets
Active target
Currently selected target
Initial training “cycle” to familiarise users with target hitting
3 test cycles in which number of targets varied from 2 each side (large) to 8 each side (small)
Each target of each size was shown once per cycle, randomly ordered
Total of 3780 test-cycle target trials across 18 users
User
Study

## Slide 38: Results: Cycles; Twist vs. Bend
Bend significantly faster than twist
Cycle has significant effect for twist but not bend
NB times on all graphs do not include final 2 seconds hold time
Chart: Cycle number (0 is training phase)
| 0 | 1 | 2 | 3
Average Time (Bend) | 1.8923 | 1.6093 | 1.6752 | 1.5534
Average Time (Twist) | 4.2926 | 3.4605 | 2.9281 | 2.6719

## Slide 39: Results: Target Number and Position
Chart: Position of Bend Target
| -0.75000000000000466 | -0.25 | 0.25 | 0.75000000000000466
2 targets | 0.685 | 0.89578 | 0.85626 | 0.61307
3 targets | 0.862 | 0.863 | 1.0239 | 0.93848 | 0.7617 | 0.83448
4 targets | 0.9563 | 1.0282 | 1.2352 | 1.2541 | 1.2947 | 1.1253 | 1.0169 | 1.0206
5 targets | 0.99378 | 1.1405 | 1.2707 | 1.6935 | 1.712 | 1.8583 | 1.6992 | 1.1116 | 1.1626 | 1.1365
6 targets | 1.0207 | 1.1239 | 1.3311 | 1.547 | 2.0303 | 3.8766 | 2.2134 | 2.3849 | 1.5548 | 1.1197 | 1.4079 | 1.4091
7 targets | 1.3483 | 1.4722 | 1.2986 | 1.7046 | 1.9732 | 2.0627 | 3.1451 | 2.0722 | 2.4061 | 2.079 | 1.5692 | 1.5627 | 1.4395 | 1.4636
8 targets | 1.3893 | 1.4787 | 1.4196 | 1.6278 | 2.3263 | 2.4171 | 2.6213 | 5.6853 | 2.4848 | 2.4587 | 2.447 | 2.087 | 1.5087 | 1.8797 | 1.7325 | 1.6619
Chart: Position of Twist Target
| -0.75000000000000455 | -0.25 | 0.25 | 0.75000000000000455
2 targets | 1.3731 | 1.3863 | 0.9355 | 1.2145
3 targets | 2.0627 | 1.6391 | 2.4457 | 1.6591 | 1.1027 | 1.3063
4 targets | 3.6599 | 2.0231 | 2.0606 | 4.2387 | 1.8591 | 1.3965 | 1.9161 | 2.2106
5 targets | 2.7182 | 2.1107 | 2.1723 | 2.6082 | 6.1309 | 3.1605 | 2.4115 | 1.6411 | 2.4552 | 1.9161
6 targets | 4.5057 | 2.9475 | 1.8481 | 2.8267 | 3.2325 | 7.6771 | 5.0977 | 2.0827 | 2.0117 | 2.1194 | 2.5817 | 2.0757
7 targets | 5.0209 | 4.0263 | 2.6279 | 2.9144 | 2.6024 | 4.2923 | 9.3466 | 3.815 | 3.5687 | 2.6211 | 2.8023 | 2.115 | 2.4424 | 3.0487
8 targets | 5.845 | 3.11 | 2.6845 | 3.1833 | 2.979 | 3.0476 | 5.0937 | 11.2344 | 3.5501 | 4.2657 | 3.1791 | 2.303 | 2.1939 | 2.6475 | 2.234 | 3.9061

## Slide 40: Results: Target Number and Position
Chart: Position of Bend Target
| -0.75000000000000488 | -0.25 | 0.25 | 0.75000000000000488
2 targets | 0.685 | 0.89578 | 0.85626 | 0.61307
3 targets | 0.862 | 0.863 | 1.0239 | 0.93848 | 0.7617 | 0.83448
4 targets | 0.9563 | 1.0282 | 1.2352 | 1.2541 | 1.2947 | 1.1253 | 1.0169 | 1.0206
5 targets | 0.99378 | 1.1405 | 1.2707 | 1.6935 | 1.712 | 1.8583 | 1.6992 | 1.1116 | 1.1626 | 1.1365
6 targets | 1.0207 | 1.1239 | 1.3311 | 1.547 | 2.0303 | 3.8766 | 2.2134 | 2.3849 | 1.5548 | 1.1197 | 1.4079 | 1.4091
7 targets | 1.3483 | 1.4722 | 1.2986 | 1.7046 | 1.9732 | 2.0627 | 3.1451 | 2.0722 | 2.4061 | 2.079 | 1.5692 | 1.5627 | 1.4395 | 1.4636
8 targets | 1.3893 | 1.4787 | 1.4196 | 1.6278 | 2.3263 | 2.4171 | 2.6213 | 5.6853 | 2.4848 | 2.4587 | 2.447 | 2.087 | 1.5087 | 1.8797 | 1.7325 | 1.6619
Chart: Position of Twist Target
| -0.75000000000000477 | -0.25 | 0.25 | 0.75000000000000477
2 targets | 1.3731 | 1.3863 | 0.9355 | 1.2145
3 targets | 2.0627 | 1.6391 | 2.4457 | 1.6591 | 1.1027 | 1.3063
4 targets | 3.6599 | 2.0231 | 2.0606 | 4.2387 | 1.8591 | 1.3965 | 1.9161 | 2.2106
5 targets | 2.7182 | 2.1107 | 2.1723 | 2.6082 | 6.1309 | 3.1605 | 2.4115 | 1.6411 | 2.4552 | 1.9161
6 targets | 4.5057 | 2.9475 | 1.8481 | 2.8267 | 3.2325 | 7.6771 | 5.0977 | 2.0827 | 2.0117 | 2.1194 | 2.5817 | 2.0757
7 targets | 5.0209 | 4.0263 | 2.6279 | 2.9144 | 2.6024 | 4.2923 | 9.3466 | 3.815 | 3.5687 | 2.6211 | 2.8023 | 2.115 | 2.4424 | 3.0487
8 targets | 5.845 | 3.11 | 2.6845 | 3.1833 | 2.979 | 3.0476 | 5.0937 | 11.2344 | 3.5501 | 4.2657 | 3.1791 | 2.303 | 2.1939 | 2.6475 | 2.234 | 3.9061
For both twist & bend
More (i.e. smaller) targets were harder
Low forces surprisingly harder (i.e. Does not follow Fitt’s Law)
For bend
Higher forces easiest

## Slide 41: Results: Target Number and Position
Chart: Position of Bend Target
| -0.75000000000000488 | -0.25 | 0.25 | 0.75000000000000488
2 targets | 0.685 | 0.89578 | 0.85626 | 0.61307
3 targets | 0.862 | 0.863 | 1.0239 | 0.93848 | 0.7617 | 0.83448
4 targets | 0.9563 | 1.0282 | 1.2352 | 1.2541 | 1.2947 | 1.1253 | 1.0169 | 1.0206
5 targets | 0.99378 | 1.1405 | 1.2707 | 1.6935 | 1.712 | 1.8583 | 1.6992 | 1.1116 | 1.1626 | 1.1365
6 targets | 1.0207 | 1.1239 | 1.3311 | 1.547 | 2.0303 | 3.8766 | 2.2134 | 2.3849 | 1.5548 | 1.1197 | 1.4079 | 1.4091
7 targets | 1.3483 | 1.4722 | 1.2986 | 1.7046 | 1.9732 | 2.0627 | 3.1451 | 2.0722 | 2.4061 | 2.079 | 1.5692 | 1.5627 | 1.4395 | 1.4636
8 targets | 1.3893 | 1.4787 | 1.4196 | 1.6278 | 2.3263 | 2.4171 | 2.6213 | 5.6853 | 2.4848 | 2.4587 | 2.447 | 2.087 | 1.5087 | 1.8797 | 1.7325 | 1.6619
Chart: Position of Twist Target
| -0.75000000000000477 | -0.25 | 0.25 | 0.75000000000000477
2 targets | 1.3731 | 1.3863 | 0.9355 | 1.2145
3 targets | 2.0627 | 1.6391 | 2.4457 | 1.6591 | 1.1027 | 1.3063
4 targets | 3.6599 | 2.0231 | 2.0606 | 4.2387 | 1.8591 | 1.3965 | 1.9161 | 2.2106
5 targets | 2.7182 | 2.1107 | 2.1723 | 2.6082 | 6.1309 | 3.1605 | 2.4115 | 1.6411 | 2.4552 | 1.9161
6 targets | 4.5057 | 2.9475 | 1.8481 | 2.8267 | 3.2325 | 7.6771 | 5.0977 | 2.0827 | 2.0117 | 2.1194 | 2.5817 | 2.0757
7 targets | 5.0209 | 4.0263 | 2.6279 | 2.9144 | 2.6024 | 4.2923 | 9.3466 | 3.815 | 3.5687 | 2.6211 | 2.8023 | 2.115 | 2.4424 | 3.0487
8 targets | 5.845 | 3.11 | 2.6845 | 3.1833 | 2.979 | 3.0476 | 5.0937 | 11.2344 | 3.5501 | 4.2657 | 3.1791 | 2.303 | 2.1939 | 2.6475 | 2.234 | 3.9061
... For twist
Highest forces start being harder too

## Slide 42: Results: Target Number and Position
Chart: Position of Bend Target
| -0.750000000000005 | -0.25 | 0.25 | 0.750000000000005
2 targets | 0.685 | 0.89578 | 0.85626 | 0.61307
3 targets | 0.862 | 0.863 | 1.0239 | 0.93848 | 0.7617 | 0.83448
4 targets | 0.9563 | 1.0282 | 1.2352 | 1.2541 | 1.2947 | 1.1253 | 1.0169 | 1.0206
5 targets | 0.99378 | 1.1405 | 1.2707 | 1.6935 | 1.712 | 1.8583 | 1.6992 | 1.1116 | 1.1626 | 1.1365
6 targets | 1.0207 | 1.1239 | 1.3311 | 1.547 | 2.0303 | 3.8766 | 2.2134 | 2.3849 | 1.5548 | 1.1197 | 1.4079 | 1.4091
7 targets | 1.3483 | 1.4722 | 1.2986 | 1.7046 | 1.9732 | 2.0627 | 3.1451 | 2.0722 | 2.4061 | 2.079 | 1.5692 | 1.5627 | 1.4395 | 1.4636
8 targets | 1.3893 | 1.4787 | 1.4196 | 1.6278 | 2.3263 | 2.4171 | 2.6213 | 5.6853 | 2.4848 | 2.4587 | 2.447 | 2.087 | 1.5087 | 1.8797 | 1.7325 | 1.6619
Chart: Position of Twist Target
| -0.75000000000000488 | -0.25 | 0.25 | 0.75000000000000488
2 targets | 1.3731 | 1.3863 | 0.9355 | 1.2145
3 targets | 2.0627 | 1.6391 | 2.4457 | 1.6591 | 1.1027 | 1.3063
4 targets | 3.6599 | 2.0231 | 2.0606 | 4.2387 | 1.8591 | 1.3965 | 1.9161 | 2.2106
5 targets | 2.7182 | 2.1107 | 2.1723 | 2.6082 | 6.1309 | 3.1605 | 2.4115 | 1.6411 | 2.4552 | 1.9161
6 targets | 4.5057 | 2.9475 | 1.8481 | 2.8267 | 3.2325 | 7.6771 | 5.0977 | 2.0827 | 2.0117 | 2.1194 | 2.5817 | 2.0757
7 targets | 5.0209 | 4.0263 | 2.6279 | 2.9144 | 2.6024 | 4.2923 | 9.3466 | 3.815 | 3.5687 | 2.6211 | 2.8023 | 2.115 | 2.4424 | 3.0487
8 targets | 5.845 | 3.11 | 2.6845 | 3.1833 | 2.979 | 3.0476 | 5.0937 | 11.2344 | 3.5501 | 4.2657 | 3.1791 | 2.303 | 2.1939 | 2.6475 | 2.234 | 3.9061
... For twist
Highest forces start being harder too
Closest target on “left” has very high times due to repeated overshooting and resetting of the 2s hold time (true for both forces)

## Slide 43: Implications of Study
Small forces not necessarily easier
  Can be explained by some flex in the device (inevitable for any device though may be higher in prototype)
  Normalise “size” of targets to reflect human perception of difficulty rather than sensor level
Up to 4 discrete bend force levels in each direction (8 total) in <1s selection time
Up to 3 discrete twist force levels in each direction (6 total) in <2s selection time

## Slide 44: Conclusions
Force sensing is a new input type for mobile devices
  Complementary to existing inputs e.g. touch, tilt
Providing interactions with feedback mimicking the force applied makes them easy to learn and use
  To explore: haptic and sound feedback
Users were able to apply forces reliably for up to 8 levels each way, and fast for 2-4 levels each way
  Interestingly, small forces are not easiest to apply

## Slide 45: SecondLight
Shahram Izadi, Steve Hodges, Stuart Taylor, Dan Rosenfeld, Nicolas Villar, Alex Butler, Jon Westhues

## Slide 46
Implicit in surface computing is that interactions are bound to the surface
Can we support interaction ‘beyond the surface’?

## Slide 55: SecondLight Video

## Slide 56: Live Demo of SecondLight
Demo runs over lunch – 5-10 at a time in Digital Living Suite (opposite LLT)
Those presenting posters please go first
I’ll be around for questions until 12 and then over lunch

## Slide 57: New hardware enables new user experiences
SenseCam
Somniloquy
Force Sensing
SecondLight